## Slide 1
Address offset (hex) | Register Name | Width (in bits) | Access | Reset Value
0 | System Clock Division Control Register (SCKDIVCR) | 32 | R/W | 2202_2222h
4 | System Clock Division Control Register 2 (SCKDIVCR2) | 8 | R/W | 40h
6 | System Clock Source Control Register (SCKSCR) | 8 | R/W | 01h
8 | PLL Clock Control Register (PLLCCR) | 16 | R/W | 1300h
A | PLL Control Register (PLLCR) | 8 | R/W | 01h
10 | External Bus Clock Control Register (BCKCR) | 8 | R/W | 00h
12 | Main Clock Oscillator Control Register (MOSCCR) | 8 | R/W | 01h
16 | High-Speed On-Chip Oscillator Control Register (HOCOCR) | 8 | R/W | 00h or 01h
18 | Middle-Speed On-Chip Oscillator Control Register (MOCOCR) | 8 | R/W | 00h
19 | FLL Control Register 1 (FLLCR1) | 8 | R/W | 00h
1A | FLL Control Register 2 (FLLCR2) | 16 | R/W | 0000h
1C | Oscillation Stabilization Flag Register (OSCSF) | 8 | R | 00h or 01h
1E | Clock Out Control Register (CKOCR) | 8 | R/W | 00h
CGC Module Base Address: 0x4001E020

## Slide 2
Address offset (hex) | Register Name | Width (in bits) | Access | Reset Value
1F | Trace Clock Control Register (TRCKCR) | 8 | R/W | 01h
20 | Oscillation Stop Detection Control Register (OSTDCR) | 8 | R/W | 00h
21 | Oscillation Stop Detection Status Register (OSTDSR) | 8 | R/W | 00h
32 | External Bus Clock Output Control Register (EBCKOCR) | 8 | R/W | 00h
33 | SDRAM Clock Output Control Register (SDCKOCR) | 8 | R/W | 00h
41 | MOCO User Trimming Control Register (MOCOUTCR) | 8 | R/W | 00h
42 | HOCO User Trimming Control Register (HOCOUTCR) | 8 | R/W | 00h
82 | Main Clock Oscillator Wait Control Register (MOSCWTCR) | 8 | R/W | 05h
85 | High-Speed On-Chip Oscillator Wait Control Register (HOCOWTCR) | 8 | R/W | 02h
3F3 | Main Clock Oscillator Mode Oscillation Control Register (MOMCR) | 8 | R/W | 00h
460 | Subclock Oscillator Control Register (SOSCCR) | 8 | R/W | 00h
461 | Subclock Oscillator Mode Control Register (SOMCR) | 8 | R/W | 00h
470 | Low-Speed On-Chip Oscillator Control Register (LOCOCR) | 8 | R/W | 00h
472 | LOCO User Trimming Control Register (LOCOUTCR) | 8 | R/W | 00h
CGC Module Base Address: 0x4001E020

## Slide 3
Address offset (hex) | Register Name | Width (in bits) | Access | Reset Value
0-F | IRQ Control Register i (IRQCRi) (i = 0 to 15) | 128 | R/W | 00h
100 | NMI Pin Interrupt Control Register (NMICR) | 8 | R/W | 00h
120 | Non-Maskable Interrupt Enable Register (NMIER) | 16 | R/W | 0000h
130 | Non-Maskable Interrupt Status Clear Register (NMICLR) | 16 | R/W | 0000h
140 | Non-Maskable Interrupt Status Register (NMISR) | 16 | R/W | 0000h
1A0 | Wake Up Interrupt Enable Register (WUPEN) | 32 | R/W | 0000_0000h
200 | SYS Event Link Setting Register (SELSR0) | 16 | R/W | 0000h
280 – 29C | DMAC Event Link Setting Register n (DELSRn) (n = 0 to 7) | 256 | R/W | 0h
300-47C | ICU Event Link Setting Register n (IELSRn) (n = 0 to 95) | 3,072 | R/W | 0h
ICU Module Base Address 0x40006000